## Slide 1: Customer-centric Energy Usage Data Management and Sharing in Smart Grid Systems
Gaurav Lahoti
University of Illinois at Urbana-Champaign, IL, USA
Daisuke Mashima
Wei-Peng Chen
Fujitsu Laboratories of America Inc., USA

## Slide 2: Smart Grid – Consumer Domain
Source: http://www.ietf.org/proceedings/77/slides/intarea-7.pdf

## Slide 3: Smart Grid – Green Button
Green Button allows customers to download their energy usage information from electricity supplier in an easy-to-understand standard XML format
Source: http://www.greenbuttondata.org/

## Slide 4: Power Usage Data - Services
The power usage data being available to customers has opened venues for 3rd party applications and specialized services
  Analyzing energy usage and provide actionable tips
  Measurement of energy-efficiency investments
  Demand-Response (DR) Aggregation
It is an active area of research and new services are constantly emerging in the market

## Slide 5: Privacy Risks
Non-intrusive Appliance Load Monitoring (NALM)
  To infer information like devices used in the house, office timings, home presence pattern, usage time of specific devices, etc.
Sample NALM
Source: http://georgehart.com/research/nalm.html

## Slide 6: Goals – Customer Centricity & Data Authenticity
Customers
Have full control over their energy usage data
Should be able to govern sharing of the data with third parties
Third Party
Should be able to ensure that the data provided by a customer is the actual data as collected and has not been modified
Utility
Should be unaware of how the energy usage data is being used by the customer

## Slide 7: Customer-centric Energy Data Utilization
Signed Energy Usage Data
Utility
Repository
Customer
Third Party
Redacted, Signed Energy Usage Data
Data Sharing, Redaction Request
Meter Reading
Signed Energy Usage Data
Customer Domain

## Slide 8: Redactable Digital Signature
Merkle Hash Tree
Signed by Utility
Data replaced by a parent hash

## Slide 9: Brute Force Attack - I
Meter reading values have a limited small range with a small upper bound
An attacker can generate a table, mapping all possible plain text values (i.e. energy usage data) to their hash values
  One table is enough for all the customers!
Keyed Hash using a Per-Customer Key
  Allows for different hash values for different customers even when a meter reading value (or a series of values) are identical.
  The key is shared with the utility company and third party to construct hash tree and calculate the root hash

## Slide 10: Brute Force Attack - II
Key is per customer and it allows mapping of identical meter reading values to same hash values for one customer
  A malicious entity can construct a meter reading to hash table for each customer as the search space is small
Random Initialization Vector (IV) and Counters
  Ensures that no two same data values of the same customer result in the same hash value
  One IV is generated for each data file
  IV is incremented by 1 for each data block
Hash Function for the leaf nodes

## Slide 11: Verifiable Redaction of Energy Usage Data
Verifiable, Redactable Energy Usage Data based on Merkle Hash Tree

## Slide 12: Security Analysis
A brute-forcing adversary will have to loop through the range of estimated data values for each hidden value
System is secure when a large number of contiguous data blocks are redacted
Under typical DR use case, only a few hours of data per day is disclosed and rest is redacted
Number of Redacted Data Blocks | Estimated Search Space Range | Number of Attempts Required
8 | 1000 | ~ 280
2 | 1000 | ~ 220

## Slide 13: Modified Green Button Information Model
0..*
UsagePoint
MeterReading
ReadingType
IntervalBlock
LocalTime Parameters
SignatureInformation
ServiceCategory
IntervalReading
ReadingQuality
IntervalHash
0..1
1
0..*
1
0..*
0..*
0..*
0..*
ElectricPower UsageSummary
ElectricPower QualitySummary
0..*
ElectricPower UsageSummaryHash
0..*
HashInformation

## Slide 14: Application for Demand-response Aggregation Service
Energy usage data is reported to utility by smart meters (e.g., every 15 min)
Data collected by utility is downloaded and stored on the trusted repository
DR event is announced
DR event is executed
Usage data is requested
Customer selects which data it wants to disclose and sends redacted data
Aggregator verifies the data and evaluates customer’s performance

## Slide 15: Summary
Customer-centric framework for energy usage data sharing
  Merkle hash tree based design for redactable, verifiable energy usage data
Prototype implementation, extending Green Button data model
Future work – Proposal for standardization in Green Button

## Slide 16: Thank You
Questions ?
For any queries, contact:
Gaurav Lahoti (lahoti2@Illinois.edu)
Daisuke Mashima (dmashima@us.fujitsu.com)