## Slide 1: A Grid-wide, High-fidelity Electrical Substation Honeynet
Daisuke Mashima, Prageeth Gunathilaka, Binbin Chen, and Edwin Tjiong
Advanced Digital Sciences Center
Singapore
Acknowledgment:
This research is partly supported by the National Research Foundation, Prime Minister's Office, Singapore under the Energy Programme and administrated by the Energy Market Authority (EP Award No. NRF2014EWT-EIRP002-040) and in part by the research grant for the Human-Centered Cyber-physical Systems Programme at the Advanced Digital Sciences Center from Singapore’s Agency for Science, Technology and Research (A*STAR).

## Slide 2: Background
For collecting and analyzing real-world attack vectors, honeypot is an effective tool used in general IT systems
  ICS/Smart Grid Honeypot system is still in an early stage
A few ICS honeypot implementations, such as CONPOT etc. are available, but none of them support the emulation of physical system in high-fidelity manner.
  Maybe OK for just collecting scanning activity, but not sufficient to retain attackers inside for slowing down attacks and/or performing longitudinal analysis

## Slide 3: Outline
Attacker models in Smart Grid communication
Design of scalable, high-fidelity, standard-compliant smart grid honeynet
Proof-of-concept implementation using open-source tools
Preliminary evaluation of realism and scalability

## Slide 4: Attacker Models in Scope
A: Attack from control center
  Compromised SCADA Master system
  Man-in-the-middle attack by other workstations
B: Attack from network
  Attack on public network infrastructure (i.e., Internet)
  Attacks on wireless network (e.g., cellular)
C: Attacks via VPN interface
  Intrusion into substation network
  Injection of malicious commands

## Slide 5: Desired Properties
Comprehensive, consistent power grid view
  Attacker may have complete visibility on smart grid communication.
  He may also have knowledge of power system laws and attempt probing.
Realistic network configuration
  IP address, MAC address, communication protocols, LAN topology etc. should look realistic
Scalability for grid-wide emulation
  Emulation of network with hundreds or thousands of substations should be possible with decent cost
Fingerprinting resistance
  Fingerprinting tools (e.g., nmap) should not be able to find hint of honeypot
  Use of virtualization technologies should not be identifiable (e.g., sufficient resource isolation among virtual instances)

## Slide 6: System Overview
*Gunathilaka, Prageeth, Daisuke Mashima, and Binbin Chen. "SoftGrid: A Software-based Smart Grid Testbed for Evaluating Substation Cybersecurity Solutions." Proceedings of the 2nd ACM Workshop on Cyber-Physical Systems Security and Privacy. ACM, 2016.
Interconnected Substation Honeypots
Each substation honeypot consists of
  Substation gateway VM
    Assumed to be fully accessible to attackers
    Connected to other substation honeypots
    Open IEC 60870-5-104 (using OpenMUC library)
  Mininet VM (Substation LAN)
    Run multiple virtual IEDs, which speak IEC 61850 MMS protocol
    Assume attackers cannot have shell access on virtual IEDs.
    Can emulate any topology and bandwidth
Monitoring functionality can be implemented on the host OS (i.e., beneath VMs)
  Not visible to attackers
Cyber-connected power grid simulation
  Provided by SoftGrid* and PowerWorld
    Emulate steady and transient state
    Can support large-scale grid model, such as 2000 bus systems (with 7,000 IEDs)
Monitoring
(e.g., Wireshark)

## Slide 7: Evaluation (1)
Comprehensive, consistent power grid view
  All honeypot substations are connected to single power flow simulator, and therefore share the consistent view.
  When control is performed, the outcome from power flow simulator is made visible within a short latency.
    Voltage and power flow are quick to reach new state so approximated with steady-state simulation
    Frequency swing takes time so transient-state simulation is used (completed within 1 seconds when 30-sec transient-state simulation is used.)

## Slide 8: Evaluation (2)
Realistic network configuration
  MAC address of honeypot gateway and virtual IEDs are configurable.
  Support widely-used standard protocols, namely IEC 60870-5-104 and IEC 61850
  Bandwidth, packet loss ratio etc., are also configurable.
  Can safely support 200 virtual IEDs per substation
  Latency on a ring topology looks realistic.
Substation GW

## Slide 9: Evaluation (3)
Fingerprinting resistance
  Scanning and OS fingerprinting by Nmap
    Substation VM is identified as Linux (2.6.32) device that opens port 2404 and 22
      Same as a commercial protocol translator (ZNX 202)
    Virtual IEDs are identifies as a device with unknown OS that opens port 102
  Shodan (https://www.shodan.io)
    After 2weeks operation, indexed as a industrial control system but not flagged as a honeypot

## Slide 10: Evaluation (4)
Isolation among Virtual Instances
  When a dedicated CPU core is allocated to each Mininet VM (substation LAN), sufficient isolation in terms of performance of emulated network is provided.
  Also found that up to 4 substation LANs can be safely run on a single Mininet VM

## Slide 11: Evaluation (5)
Scalability / Operational Cost
  Theoretically, we can host up to 16 honeypot substations (GW and LAN) on a quad-core PC
    The number is close to high-volt. substations in Singapore.
  On National Cybersecurity Lab testbed (https://ncl.sg), we tested operation of 18 substations per node
    Given CPU usage on the node is less than 30%, we can host more than 36 substations safely.
    Operational cost to run a 200 and 1,500 substation system are US$390/month and US$2,700/month respectively.
  Deployable also on Amazon EC2 (with minor modification).

## Slide 12: Conclusions
We designed and implemented, scalable smart grid honeynet with high-fidelity power system simulation
Looking for industry and academic partners for extensively evaluating and enhancing the system.
Future enhancement includes:
  Collection and analysis of real-world attacks
  Incorporation of mechanical/actuation latency models
  Realism evaluation through comparison of hardware-based power grid testbed
  Generation of dummy, but realistic, SCADA/substation LAN traffic
  Release honeypot codes as add-on for open-source SoftGrid project (URL: http://www.illinois.adsc.com.sg/softgrid/)

## Slide 13: Thank you very much!
Questions?
For any interest, suggestion, or request, please feel free to contact us at:
  Email: softgrid@adsc.com.sg

## Slide 15: Smart Grid Honeypot/net Use Cases (1)
To counter Attack A:
  In the control center, we can set up dummy SCADA Master and/or workstation that are intentionally made vulnerable
    E.g., they may look like a back-up system
  Outgoing traffic from those machines are routed to Smart Grid honeynet
    Can be done by means of router configuration or software-defined network technologies
SCADA
Master
Dummy
SCADA
Master
Dummy
Workstation
Control Center
Real
system
Smart Grid Honeynet

## Slide 16: Smart Grid Honeypot/net Use Cases (2)
To counter Attack B:
  Some of honeypot substations can be connected to the Internet (or other type of public WAN)
  Some of honeypot substations can be equipped with cellular communication module
To counter Attack C:
  Expose VPN interface of substation gateway, configure with weak credential, to public
Smart Grid Honeynet
Substation Honeypot
Substation Honeypot
Substation Honeypot
Substation Honeypot
Substation Honeypot
Substation Honeypot
Substation Honeypot
WAN /
Internet